Program Description

1. Introduction

Builtin commands include:
- cd – move/change directory
- clr – clear screen
- dir – list out directories and files
- environ – prints out the env variables
- echo – prints back out items entered after “echo”
- help – display help message
- pause – pause till user press enter
- exit – exit the shell

External commands:
Assume we have an executable “hello” compiled from “hello.c”, the shell can execute “hello” by having the user type in:
<prompt>$ ./hello

2. Program design

Source files consist of 4 main ones:
- main.c
- function.c
- header.h
- Makefile
Detail
main.c
Initializes the shell and run a continuous loop asking for new commands. If a command string is successfully taken in and tokenized, main will direct the token list to shell_execute(), which lies in function.c

function.c
Contains the huge shell_execute() function and all functions the perform builtin functionalities.
Shell exec() parses the tokenized argument list, check for special symbols, and determine a builtin or an external command will be executed.
Other functions (return void) lies in function.c includes:
- int shell_execute(char** args_list);
- void shell_cd(char** args_list);
- void shell_pause(char** args_list);
- void shell_echo(char** args_list);
- void shell_help(char** args_lis);
- void shell_environ(char** args_list);
- void shell_clr(char** args_list);
- int is_dir(char *path_name);
- void shell_ls(char** args_list);
- void shell_exit(char** args_list);
- int exec_pipe(char **args, int p_indx);
3. Test plan

The process of building this shell starts from buiding the frame of execution, moving on to builtin commands, external commands, and finally, functions for I/O redirection, pipe, and background run symbols.

Core tests/checks in any new built:
- Error check every time a system_call() is called
- Open a non-existent file/folder
- Execute an invalid command, or invalid version of a builtin
- fork() or pipe() failing
- exec() fails to launch
- memory allocation & deallocation

Tests for each function:

1. Test read_dictionary()
2. Test network setup